## Slide 1: MINI PIANO USING ARDUINO
Khushi Jha (2019BTCS036)

## Slide 2: INTRODUCTION TO ARDUINO
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
Arduino Boards are able to read inputs - light on a sensor, a finger on a button, or a Twitter message - and turn it into an output - activating a motor, turning on an LED or publishing something online.

## Slide 3: The reasons behind people preferring Arduino over others are:
Inexpensive
Cross-platform
Simple and clear programming environment
Open source and extensive software

## Slide 4: Introduction to Project:
The project is Mini Piano using Arduino, this piano is pretty much plain with just 7 push buttons and 8 ohm speaker. Mini Piano is a musical device which play tunes of different frequency. This mini piano is made with 7 customizable buttons allowing you to play any frequency and tone you want. It uses the tone () function of Arduino to create various types of piano notes on the speaker.

## Slide 5
COMPONENTS:
The list of components required to build the project is as follows:
Arduino Nano R3
Breadboard
7 * Push Button switches
8 ohm Speaker
Cable
18 * Jumper wires

## Slide 6: Circuit Diagram
The wiring of the circuit goes in the following steps as mentioned:
| Button | Arduino Nano |
|------------|-------------|
| Button 1 | D4 |
| Button 2 | D5 |
| Button 3 | D6 |
| Button 4 | D7 |
| Button 5 | D8 |
| Button 6 | D9 |
| Button 7 | D10 |

## Slide 7: Code
#define T_C 262
#define T_D 294
#define T_E 330
#define T_F 349
#define T_G 392
#define T_A 440
#define T_B 493
const int C = 10;
const int D = 9;
const int E = 8;
const int F = 7;
const int G = 6;
const int A = 5;
const int B = 4;
const int Buzz = 11;
const int LED = 13;

## Slide 8
void setup()
{
pinMode(LED, OUTPUT);
pinMode(C, INPUT);
digitalWrite(C,HIGH);
pinMode(D, INPUT);
digitalWrite(D,HIGH);
pinMode(E, INPUT);
digitalWrite(E,HIGH);
pinMode(F, INPUT);
digitalWrite(F,HIGH);
pinMode(G, INPUT);
digitalWrite(G,HIGH);
pinMode(A, INPUT);
digitalWrite(A,HIGH);
pinMode(B, INPUT);
digitalWrite(B,HIGH);
digitalWrite(LED,LOW);
}

## Slide 9
void loop()
{
while(digitalRead(C) == LOW)
{
tone(Buzz,T_C);
digitalWrite(LED,HIGH);
}
while(digitalRead(D) == LOW)
{
tone(Buzz,T_D);
digitalWrite(LED,HIGH);
}
while(digitalRead(E) == LOW)
{
tone(Buzz,T_E);
digitalWrite(LED,HIGH);
}
while(digitalRead(F) == LOW)
{
tone(Buzz,T_F);
digitalWrite(LED,HIGH);
}
while(digitalRead(G) == LOW)
{
tone(Buzz,T_G);
digitalWrite(LED,HIGH);
}
while(digitalRead(A) == LOW)
{
tone(Buzz,T_A);
digitalWrite(LED,HIGH);
}
while(digitalRead(B) == LOW)
{
tone(Buzz,T_B);
digitalWrite(LED,HIGH);
}
noTone(Buzz);
digitalWrite(LED,LOW);
}

## Slide 10: IMAGES

## Slide 12
THANKYOU